Point↔face proximity
p
N
N
N
a
|d|>dmax
p’
|d|<dmax
u+v+w≠1
b
c
c
c
OUI
NON
given a distance dmax, p is detected as « near » triangle abc is its unsigned distance to plane
Pabc, containing a,b and c, is less than dmax and if p’, the projection of p onto Pabc lies inside
triangle abc. In other words, if p’ barycentric coordinates u,v,w are such that u+v+w=1 and
each of u,v and w are in [0;1]. p will be flagged as « behind » if its signed distance to Pabc < 0

---
Point↔edge proximity
given a distance dmax, p is detected as « near » edge ab if its unsigned distance to line
Lab, passing through a and b, is less than dmax and if p’, the projection of p onto Lab lies inside ab. p’ is such that pp’ is orthogonal to Lab.
triangle abc. In other words, if p’ barycentric coordinates u,v,w are such that u+v+w=1 and
each of u,v and w are in [0;1]. p will be flagged as « behind » if its signed distance to Pabc < 0

---
Point ↔ vertex proximity
v
v
YES
NO
given a distance dmax, p is detected as « near » vertex v if its distance to v is less than dmax

---
Point↔mesh proximity functor
- Called for each point p with the nearest element (triangle, edge or vertex) to p.
- Edges and vertices may be disabled, then only triangles are considered
- Functor always called with vertex indices v0, v1 and v2
  - V1 and v2 are -1 for vertex proximlity (consider only v0)
  - V2 is -1 for edge proximity (consider only v0 and v1)
  - all three indices are = -1 for triangle proximity
- see src/mesh/trimesh_particle_proximity.cu for example usage